## Slide 1
Applied Microprocessor Lab VS Code Env Setting
전력전자연구실

## Slide 2: Index
CubeSTM32 into VS Code
Make a Project with CubeMX
Build and Download into MCU

## Slide 3: CubeSTM32 into VS Code
Launch VS Code
  Do not use Onedrive / Gdrive / 한글 in Project Path to avoid permission issues.
  Turn off extensions you will not use

## Slide 4: CubeSTM32 into VS Code
Pros and Cons
Pros
  Can use VS Code
  Works on all OS (Windows / Mac / Linux)
  Free to use / Opensource
Cons
  No official technical support or warranty
  Many companies prefer paid tools with professional support

## Slide 5: CubeSTM32 into VS Code
Install extensions
  Search ‘stm’ in extension menu in VS Code
  Install Prerequisites

## Slide 6: CubeSTM32 into VS Code
Install extensions
  STM32CubeCLT : ARM C Compler, Debugger, Library
  STM32CubeMX : Help you make STM Projects
  STMCUFinder : Find and Download into mcu board

## Slide 7: Make a Project with CubeMX
Make a new C Project with CubeMX
  Login first myST

## Slide 8: Make a Project with CubeMX
Make a new C Project with CubeMX
  Select the right board (check model number of your board)
Double click here

## Slide 9: Make a Project with CubeMX
Make a new C Project with CubeMX
  TrustZone is not covered in this class (need for product-level security) (It may not appear depending on the board)
  Press OK if no error occurs
  LED and Button, useful for build testing

## Slide 10: Make a Project with CubeMX
Make a new C Project with CubeMX
  Use the exact path and select Cmake toolchain
  Pinout and clock configuration will be covered later

## Slide 11: Make a Project with CubeMX
Make a new C Project with CubeMX
  This option increases the size of project (but ok)
  CubeMX generates useful C code automatically Enabling this option keep your codes (Enabled by default)
  Click this button to generate code

## Slide 12: Make a Project with CubeMX
Make a new C Project with CubeMX
  Press OK if no error occurs

## Slide 13: Make a Project with CubeMX
Return to VS Code
  Always reload VS Code when something new is installed
  Type >reload or press Ctrl + Shift + P and search for “reload

## Slide 14: Make a Project with CubeMX
In VS Code
  In menu “STM32 VS Code Extension” Extension, we have to import CMake project but sometimes it does not work at first
  Similar to reload, search for >cubeclt and configure the path

## Slide 15: Make a Project with CubeMX
In VS Code
  If you installed CubeCLT successfully, you can select C:/ST/STM32CubeCLT_X.XX.X (Linux/MacOS : auto-detected)

## Slide 16: Make a Project with CubeMX
CubeCLT Configured
  Now you can import your project and VS Code will complete the remaining setup that CubeMX did not

## Slide 17: Make a Project with CubeMX
Import CMake Project
  If “cmake --version” command not works, quit and re-open vscode

## Slide 18: Build and Download into MCU
CMake Project Imported
  This is made by VS Code Ext
  - This is made by CubeMX

## Slide 19: Build and Download into MCU
Build Test
  Now you can compile whole .c source codes and get .elf binary

## Slide 20: Build and Download into MCU
Build Test
  (Compiling messages)
  They want to disable something, let them do it

## Slide 21: Build and Download into MCU
Build completed messages
  [build] Build finished with exit code 0
  - You can also check the compiled binary (.elf)

## Slide 22: Build and Download into MCU
Download .elf binary into your board
(사진추가예정)

## Slide 23: Finish
You can find my source code and installation video on his Github